# SAC Protocol v2.0 Jorge Gómez Arenas <jorge@sindormir.net>
### Generic Datagram:
Header byte					First payload byte					Second payload byte					Parity byte
H	S	S	S	D	D	D	P		H	H	T	L	L	L	L	P		H	H	L	L	L	L	L	P		P	P	P	P	P	P	P	P

H: Header, S: Source, D: Destination, T: Type of packet, P: Parity bit, L: payload
#### Datagram Type 0 (Status datagram)
First payload byte					Second payload byte
H	H	0	p	p	p	p	P		H	H	s	s	g	g	g	P

p: Position, s: Speed, g: Destination exit
#### Datagram Type 1 (Control datagram)
First payload byte					Second payload byte
H	H	1	C	C/L	C/L	C/L	P		H	H	L	L	L	L	L	P

C: Control packet type, L: payload
##### Datagram Type 1, Control packet type 1XXX (ACK datagram)
First payload byte					Second payload byte
H	H	1	1	c	c	c	P		H	H	c	c	c	c	c	P

c: Checksum of the packet being ACK'd
##### Datagram Type 1, Control packet type 01XX (Manual motor control)
First payload byte					Second payload byte
H	H	1	0	1	Pm	Pd	P		H	H	m	s	s	d	d	P

Pm: Permanent movement bit, Pd: Permanent direction bit, m: 0 → Backward, 1 → Forward. ss: 00 → Stop, 01 → min, 10 → med, 11 → max. dd: 00 → Straight, 01 → Right, 10 → Left
##### Datagram Type 1, Control packet type 0011 (SAC Control protocol)
First payload byte					Second payload byte
H	H	1	0	0	1	1	P		H	H	m	m	m	m	m	P

m: Message: xxx10 → PIP Request,	xxx11 → PIP ACK,	xx1xx → RTV Begin, xx0xx → RTV End
##### Datagram Type 1, Control packet type 0010 (Remote control command)
First payload byte					Second payload byte
H	H	1	0	0	1	0	P		H	H	s	s	g	g	g	P

s: Speed, g: Destination Exit
##### Datagram Type 1, Control packet type 0001 (Status request).
First payload byte					Second payload byte
H	H	1	0	0	0	1	P		H	H	x	x	x	x	x	P

x: Unused bits
##### Datagram Type 1, Control packet type 0000 (Heartbeat packet).
First payload byte					Second payload byte
H	H	1	0	0	0	0	P		H	H	x	x	x	x	x	P

x: Unused bits
# SAC v2.0 Definición de funciones:

Void PrepareDatagram(sac2_datagram)
Input: Datagrama en forma de estructura
Output: txbuf cargado, parity byte cargado en estructura
Función: Codifica la estructura en forma de datagrama
Llamada por: SendDatagram
Void SendDatagram(sac2_datagram, int timeout)
Input: Datagrama a enviar en forma de estructura
Output: Dato enviado y confirmado o error